## Slide 1: ENGI 301 QuadCopter PB Cape Proposal
19th November, 2018
Walker Grimes

## Slide 2: Background Information
  I have already implemented the PB with Drone motors.
  The PB lacks several critical systems that standard flight control boards have
    Accelerometer
    Gyroscope
    Barometer
    Altimeter
    GPS
  The goal of this project is to design a cape for the PB to meet these needs
https://www.hackster.io/patrickpoirier51/pocketpilot-an-autopilot-based-on-the-25-pocketbeagle-1fa14b
Fig 1: Pocket Pilot

## Slide 3: Board Functionality
This board will serve two purposes:
  The PB doesn’t have the required instrumentation for proper flight control. This board will incorporate the three major chips (GPS, Accel/Gyro, Altimeter)
  The PB PWM pins are far apart and connecting the motors required a homemade breakout board. The cape will have a cluster of pins to simplify connections

## Slide 4: Functional Block Diagram
1300mah,14v, 4s LiPo Dynogy Battery
Accel/Gyro
MPU6050
PocketBeagle
I2C
M1
M2
M3
M4
BR2205 Motors
Altimeter
Level
Shifter
GPS
I2C
PWM
Vin
6 Pin JST-SH (UART)
100 mil 3 prong male headers
(GND,nc,sig)
1.8V
(GND,Vin,GND)
3.3V
PDB
3.3V
5V BEC
Motor Power Out
Micro USB
USB1 Port (P1_5,7,9,11,13,15)

## Slide 5: Mechanical Diagram
PocketBeagle
Cape
2.21”
Same Size
1.38”
The cape will go on top of the PB
The connection will be accomplished by two 36 pin male headers on the bottom of the board matching the female headers on the board